Parallel LFSR Notes

What tf is it?
- Shift Register where input bit is a linear function of previous states
- Parallel LFSRs can shift multiple bits in a single clock cycle
- Increases speed and complexity

Making them high SPEED
- Pipelining
- Break logic into stages separated by registers
- Reduces critical path delay
- Higher clock frequency
- Split 8 bit stage into 2 x 4 bit stages
- Optimize Logic Design
- Boolean Minimization
- Karnaugh Maps
- For large parallel widths use look-ahead techniques
- Technology Scaling
- Lower transistor size to increase speed and lower gate delays
- Clock Distribution
- Balanced clock tree
- Ensure all registers update simultaneously

Making them low power
- Clock Gating
- Disable clock signals to unused portions of the LFSR when not all outputs are needed
- Dynamic Voltage & Frequency Scaling (DVFS)
- Adjust supply voltage and clock frequency based on throughput demand
- At low speeds, reducing Vdd quadratically cuts dynamic power
- P = CV^2f
- Minimize Switching Activity
- Choose a polynomial with fewer taps
- Reduces XOR operations, lowering power
- Optimize initial seed to avoid high-toggle patterns
- Subthreshold Design
- For ultra low power designs, operate transistors in the subthreshold region
- Sacrifices speed but can save more power

Making them reconfigurable
- Programmable Feedback Polynomial
- Use MUXes or programmable logic (LUTs in an FPGA)
- Variable Parallel Width
- Design with modular blocks that can be enabled/disabled
- Configuration register can switch between modes for 4 bit, 8 bit, 16 bit, etc
- Control Logic
- Add a small FSM (Finite State Machine) to adjust parameters on the fly
- Switching polynomials or parallel widths based on input signals or software commands

Tips and Trade-Offs
- Speed vs Power
- Pipelining increases speed but adds registers, increasing area and static power
- Solution: Only pipeline critical paths
- Reconfigurability and Complexity
- More flexibility increases area and sometimes delay due to MUX overhead.
- Keep reconfiguration minimal if aiming for performance
- Testing (NOT REQUIRED FOR PROJECT)
- Simulate with Verilog/VHDL
- To verify timing - Synopsis Design Compiler
- To verify power – PowerArtist
- Prototype well with the Xilinx Zynq FPGA

Applications
-

LFSR Performance
Section 1 - Introduction
- Built In Self Test (BIST)
- Adding a little overhead to the circuit for the purpose of testing
- Removes the use of complex external testing components
- Used to produce irregular patterns for testing a VLSI circuit
- Static Power Dissipation
- Product of leakage current and source voltage
- P(static) = V(dd) * I(leakage)
- Short CIrcuit Power Dissipation
- Occurs during switching when current flows from power supply to ground
- P(short) = V(dd) * I(short)
- Dynamic Power Dissipation
- 90% of overall power consumption and is due to switching activities
P(dynamic) = β * C * V(dd) * 2 * F
β = Exchanging action per node
C = Switched capacitance
F = Switches per second
V(dd) = Supply voltage

Section 2 - Linear Feedback Shift Register
- yea

Section 3 - Bit Swapping LFSR
- If nth bit is 0 then bits swap
- If odd bit is 0 then all remaining bits swap
- If even bit is 0 then only next bit swaps
- If nth bit is 1 then bits don’t swap

Section 4 - Arithmetic Weight Random Test Pattern Generator