Input Bias Current
- In reality, the two input currents of an OP-AMP are NOT zero
- Bias Current is the average of the two input currents
- We imagine that there are current sources within the OP-AMP that draws current into each	input

Offset Current
- Is equal to the difference between the two input currents of an OP-AMP
-

Slew Rate
- The maximum rate of voltage change that can be generated by the op-amp’s output.
- It is measured as voltage relative to time (volts per microsecond)
- Is because of the charge delay from capacitors and inductors
- It is found by calculating the SLOPE of a voltage over time function

For linear operation
- slew rate is greater than or equal to omega*Vi

Common Mode Rejection Ratio
- Adiff divided by Acm ideally goes to infinity